# Violin

# The blanks

Finger board (hardwood)

42,6 mm

9,6 mm

270,1 mm

tailpiece (hardwood)

41,3 mm

112,0 mm

11,6 mm

Top and back (tone wood) (Fichte)

216,5 mm

355,4 mm

13,8 mm

Neck  (Maple)

23,7

103,0

317,4

The bridge

see bridge.ai files the number refers to the mm between the legs.

I use hornbeam,  it is a bit heavy but it sounds bright

The saddles

Made of Fichte ( I use what is left the top or back )

Sides

520 mm long

36  mm wide (32 needed).

5 mm bending triplex

aug 2014-08-15